RAISELIFT OY

PEAT PRODUCTION MACHINERY

RAISELIFT OY

RAIVALANTIE 524

39920 SUOMIJÄRVI

FINLAND

TEL. 	+358 2 544 4141

+358 400 126 332

FAX 	+358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

# MILLED PEAT HARVESTER/STOCKPILING WAGON M-40 V

Mechanical milled peat harvester/stockpiling wagon that collects peat from the ridge.

The wagon is emptied from the bottom and peat is stockpiled with the wagon into a compact stockpile. Bottom unloading is patented. Loading conveyor is equipped with a flexible top and back part to prevent damages caused by tree stumps.

TECHNICAL DATA:

Required engine output		85 kW

Working capacity		150-250 m3/h

Loading capacity		3-4 min/37 m3

PTO			1000 rpm

Weight			5800 kg

Tires			width 774, height 1850, 4 pcs

Hauling chassis		mechanical power transmission

Loading conveyor width		1300

Loading conveyor’s power transmission: with two fluid motors

Loading conveyor’s revolution counter

Oil pressure gauge

Oil temperature gauge

Wide axis, distance of the wheel fastening flanges: 2800

Finishing 			sand blasting, priming and topcoating

Peat load 			37 m3

Tank capacity		40 m3

Load fill-up indicator

Tank width			4000

Tank length		3100

Overall width		4850

Overall length		9800

Overall height		4750

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

HARVESTER M-30

Mechanical milled peat harvester that collects peat from the ridge.

The harvester is emptied from the bottom and peat is stockpiled with the harvester into a compact stockpile (bottom unloading patent). Loading conveyor is equipped with a flexible top and back part to prevent damages caused by tree stumps (patent).

TECHNICAL DATA:

Required engine output		70-80 kW

Capacity			70-140 m3/h

Peat load			27 m3

Tank capacity		30 m3

Weight			4200 kg

Loading conveyor width		1000

Hydraulic loading conveyor’s power transmission

PTO			1000 rpm

Tires			600/50-22.5/8 ELS L-1 TL 8 pcs

Loading conveyor equipped with a revolution counter

Load fill-up indicator

Tank width			3400

Tank length			3100

Overall width		4200

Overall length		8000

Height			4525

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

MILLED PEAT HARVESTER/STOCKPILING WAGON I-40 V

Pneumatic milled peat harvester/stockpiling wagon that collects peat straight from the surface of the field.

The wagon is emptied from the bottom and peat is stockpiled with the wagon into a compact stockpile. Bottom unloading is patented.

Blower’s power transmission is equipped with a fluid clutch (no vee belts). Suction pipe is equipped with flexible joints to prevent trembling damages. Nozzle is lifted up in a way that the blockages that have remained in the nozzle during the loading phase will fall off. Load fill-up indicator is equipped with an illuminated screen.

TECHNICAL DATA:

Working width 		3000

Driving speed 		10-14 km/h

Required engine output 		min. 80 kW

Working capacity 		120-200 m3/h

Mechanical blower’s power transmission

PTO			1000 rpm

Weight 			5500 kg

Tires			width 774, height 1850, 4 pcs

Wide axis, distance of the wheel fastening flanges: 2800

Hauling chassis, mechanical power transmission

Blower’s suction vent ( 900, nozzle’s suction vent 80 x 1500 2 pcs

Airspeed in the nozzle’s suction vent 	50 m/s

Blower revolution 1546 rpm, amount of air 16.5 m3/s

Blower’s required engine output 	47 kW

Air and material controls (polythene sheets) inside the roof part

Finishing			sand blasting, priming and topcoating

Peat load 			36 m3

Tank capacity 		40 m3

Tank width 			4000

Tank length 		3100

Overall width 		6800

Overall length 		9000

Overall height 		5250

Outer width of the train of gears 	4850

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

HARVESTER I-40V I-80V SPECIAL CHARACTERISTICS

- Bottom unloading: Unloading can be performed by driving to the top of the stockpile, growing the stockpile without using a separate stockpiling machine. The formed stockpile is compact, peat preservability improves and there is no hazard of spontaneous combustion.

- Nozzles: Nozzles are on the right side viewed from the back of the harvester, because this makes it easier for the driver to follow the nozzles and their functioning. Tractor’s hydraulics control system is in the cockpit, on the right side viewed from the back. When the driver’s right hand is on the control switch, he is already partly turned to the observation direction of the nozzles. In consequense the drive becomes more comfortable. Nozzle damages have been minimized with hanging and lifting machinery. The suction vent remains downwards when the nozzles are lifted up. Blockages that have remained in the nozzle during the loading phase will fall off.

- Sealing of the tank and suction tubes have been performed with special attention and care. This way the blowers’ capacity losses have been removed. Leaking of the tank’s seals is one reason for strong dust discharge in the blower.

- The tank’s and cyclone’s sheet metal have been stiffener patterned to prevent heat distortions during welding and changes caused by low pressure. This way also the harvester’s exterior features are clean-cut. All parts have been sand blasted, primed and topcoated.

- Blower’s power transmission: transmission is equipped with a fluid clutch (no vee belts).

MILLED PEAT HARVESTER/STOCKPILING WAGON I-80V

Pneumatic milled peat harvester/stockpiling wagon that collects peat straight from the surface of the field.

The wagon is emptied from the bottom and peat is stockpiled with the wagon into a compact stockpile. Bottom unloading is patented.

Blower’s power transmission is equipped with a fluid clutch (no vee belts). Suction tube is equipped with flexible joints to prevent trembling damages. Nozzle is lifted up in a way that the blockages that have remained in the nozzle during the loading phase will fall off. Load fill-up indicator is equipped with an illuminated screen.

TECHNICAL DATA:

Working width 		3000

Driving speed 		10-15 km/h

Required engine output 		min. 100 kW

Working capacity 		200-300 m3/h

Mechanical blower’s power transmission

PTO 			1000 rpm

Tires			width 774, height 1850, 8 pcs

Outer width of the train of gears 	4850

Wide axis, distance of the wheel fastening flanges: 2800

Towing machine wheel tractor, equipped with stockpile levelling butt sheet, min 95 kW

Hauling front wagon, mechanical power transmission

Blower’s suction vent ( 1120, nozzle’s suction vent 100 x 1500 2 pcs

Airspeed in the nozzle’s suction vent 	50 m/s

Blower revolution 1216 rpm, amount of air 19.9 m3/s

Blower’s required engine output 	60 kW

Finishing 			sand blasting, priming and topcoating

Peat load 			60 m3

Weight 			10000 kg

Tanks’ capacity 		40 m3 x 2 = 80m3

Tanks’ width 		4000

Tanks’ length 		3100

Overall width 		6800

Overall length 		19300

Overall height 		5250

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

PRODUCTION MILLER

Working width		8.3–9 m

Required engine output		60-90 kW

Blade pipes’ diameter to the tip of the blades ( 250 mm

* Blade equipment		hook blade that forms particles, model 2006

Milling depth		5-20 mm

Rotating speed		1000 rpm

Capacity			4-9 ha/h

Power transmission		mechanical

Transmission			cone cylinder gear SL 2160

Right side element turned 5(

Towing machine		wheel tractor

Front wheels’ diameter		( 850 mm

Back adjustment wheel diameter	( 1160 mm

Driving speed		5-10 km/h

Weight			2650 kg

Tires in the front		400-15.5, 12 pcs

Back adjustment wheel		500/60/22.5, 1 pc

* Model protected

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

PRODUCTION MILLER

Working width		6 m

Required engine output	 	60-85 kW

Blade pipes’ diameter to the tip of the blades ( 250 mm

* Blade equipment 		hook blade that forms particles, model 2006

Milling depth		5-20 mm

Rotating speed		1000 rpm

Capacity			3-6 ha/h

Power transmission		mechanical

Transmission			cone cylinder gear SL 2160

Towing machine		wheel tractor

Support wheels’ diameter		850 mm

Back adjustment wheel diameter 	1160 mm

Driving speed		5-10 km/h

Weight			2100 kg

Tires in the front 		400-15.5, 10 pcs

Back adjustment wheel 		500/60/22.5, 1 pc

* Patent application

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

- Miller’s middle part

- Transmission

- Milling depth adjustment

- Transmission fastening

- Axis 1 ¾” 6 splines

- Side element turned 5(

- Hook blade, patent application

CONE CYLINDER GEAR

Type			SL 2160

P=			110 kW/n1=1000 min-1

n2=			760 min-1

Using environment’s temperature 	0 - +40(C

Amount of lubricant oil	 	16 l

- Equipped with an oil height gauge and oil temperature gauge

Weight			294 kg

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

PRODUCTION MILLER variable aileron accessory

Working width 6 – 8.5 – 9 m, also a model that is towed with a jib is manufactured.

With long variable ailerons: KÄ-18, model 2010

Aileron length 1500

Hydraulic aileron lifting

Wheels 400 – 15.5” height 850 12 pcs

Wheels 700/22.5” height 1200 2 pcs, in the towable model 500/22.5” height 1200 2 pcs

Benefits of a miller equipped with variable ailerons:

- The driver can observe the amount of peat that the miller blade has released from the harrowed ridge.

- Saves one harrowing time and the drying begins immediately.

- In the case of rain immediately after the milling, harrowed ridge does not stick to the field and new milling is not needed.

Harrow’s working width according to the miller’s working width

BROACHING (12

DEEP 15 (1 PC)

(FROM THE FRONT)

MILLER BEARING HOUSING, MODEL 2003

Oiling separately for axis seals

The seals and the bearing are in individual oiling compartments and can be oiled separately.

REQUIREMENT: 6 PCS/MILLER

PEAT PRODUCTION MILLER

HOOK BLADE THAT FORMS PEAT PARTICLES

MODEL 2006

PEAT FIELD’S SURFACE

UTILITY MODEL 7162

# RIDGER KA-10 T

Towing machine		wheel tractor

Required engine output		50-70 kW

Hydraulics			1 x single-acting and 1 x double-acting

Working width		9.6 m

Ditch edge wheels		400 R 15.5” height 850 2 pcs

Lifting wheels		500/60 R 22.5” height 1190 2 pcs

Weight			2200 kg

Ridging capacity		15-25 ha/h, two ridges to a sedge

The ridges can be combined into one ridge in the middle of the sedge.

Linking aileron elements 		6 pcs

Ridge width hydraulically adjustable 	570-1000

One cylinder

Hydraulic lifting, four cylinders

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

# MILLED PEAT HARROW KÄ-18

Model 2010

A long wing that forms harrowed ridge during fast drive.

Wing length			1500

Driving speed		10 – 12 km/h

Towing machine		wheel tractor

Required engine output		60 kW

Hydraulics 3 x double-acting usage

Harrowing capacity		18 – 22 ha/h for harrowed ridge

Working width		18.4 m

Wheels			400/15.5” height 850 4 pcs

700/22.5” height 1200 2 pcs

Amount of turning elements 	74 pcs (plastic)

Variable ailerons are equipped with a bearing and aileron’s best fitness to the surface of the field is attained.

Weight 			2800 kg

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

HARROW

KÄ 9

TRACTOR TRAILER REVERSAL TRANSMISSION

- Gear ratios 1:1-5:1

- Change of gearing by changing the upper axis bearing housing and sprocket.

- Power transmission connection hydraulically

- Switch inside the case

- Fastening to a welded sheet in the trailer’s towing boom with four M 20 bolts

- Hydraulics pump with an overrunning clutch, fastening possibility for an upper axis

- No daily maintenance

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

# REDUCTION GEAR

Type		SL 92 FE

Gear ratio		3.14-1

Weight		60 kg

Length		528

(		304

Amount of lubricant oil 	3.5 l

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

# COMBINATION TRAILER YPV-50

(STOCKPILING WAGON)

Load space			50 m3

Length			15000

Height			3200

Load spaces’ width		4100

Overall width		4850

Front trailer weight		4000 kg

Back trailer weight		3000 kg

Tires 			width 774, height 1850, 8 pcs

Hydraulics			3 x double-acting

Required engine output		85 – 100 kW

Shifting capacity in Haku method, stockpiled 3300 m3/24h/combination trailer.

Hauling front trailer, mechanical power transmission.

Wide axis, distance of the wheel fastening flanges: 2800

Unloading			bottom unloading method

Patent no. 61913

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

# TRAILER K 35

Capacity	with forage rims	31 m3

with grain rims	21 m3

Length	8550

Width	2600

Height	3300

Weight	5800 kg

- Chain unloader uses separate hydraulics unit.

- Hydraulic opening and locking of the backboard.

- Carrying capacity 16000 kg.

- Breaks in the bogie’s front wheels.

- Basic boards’ sheet: strength profile, hardness 500 HB.

- Tires 700/45 – 22.5 PR 12 ELS L-1 TL Nokia 4 pcs.

- Hydraulics: required PTOs 1 x single-acting.

- Suitable for use in peat production with extension tire equipment.

- Surface treatment: sand blasting and painting.

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

HARVESTER M-30 SP

Mechanical milled peat harvester that collects peat from the ridge.

The harvester is emptied with a chain unloader to the right side. Loading conveyor is equipped with a flexible top and back part to prevent damages caused by tree stumps (patent).

Required engine output		85 kW

Capacity			120-170 m3/h

Hydraulics 			required PTOs 1 x single-acting, 1 x double-acting

Loading conveyor width		1000

Hydraulic loading conveyor’s power transmission: with two fluid motors

Loading conveyor’s revolution counter

Hydraulic usage of the chain unloader

PTO			1000 rpm

Tires			600/50 – 22.5/8 ELS L-1 TL, 8 pcs

Load tank’s capacity 		30 m3

Load fill-up indicator

Load space’s side sheet same as in the trailers M-40V, I-80V, and I-40V.

Surface treatment		sand blasting, priming and topcoating

Peat load			28 m3

Overall width		4700

Length			8000

Height			4600

Weight			5500 kg

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

HARVESTER M-30 SP V

Mechanical milled peat harvester that collects peat from the ridge.

The harvester is emptied with a chain unloader to the right side. Loading conveyor is equipped with a flexible top and back part to prevent damages caused by tree stumps, patent no. 861614.

Required engine output		85 kW

Capacity			120-170 m3/h

Hydraulics 			required PTOs 1 x single-acting, 1 x double-acting

Loading conveyor width 		1300

Hydraulic loading conveyor’s power transmission: with two fluid motors

Hydraulic usage of the chain unloader

PTO 			1000 rpm

Tires 			width 774, height 1850, 4 pcs

Load space’s side sheet same as in the trailers M-40V, I-80V, and I-40V

Load fill-up indicator

Surface treatment		sand blasting, priming and topcoating

Tank capacity		30 m3

Peat load			28 m3

Overall width		4850

Length			8000

Height			4600

Weight			6500 kg

Hauling chassis

Mechanical power transmission

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

COMBINATION TRAILER YPV 50 S

Load space			50 m3, maximum load 56 m3

Length			16140

Height			3100

Width			3900

Weight			front trailer 4000 kg

Weight			back trailer 3000 kg

Front trailer			hauling, mechanical power transmission

Turning circle		16 m

Unloading			chain unloading to the right side, fluid engine

Tires			30.5” x 32, 8 pcs

Required hydraulics		3 x double-acting

Required engine output		85 kW

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

MILLED PEAT SCREENING STATION JTSA 400

Screening capacity 	400 m3/h

Length 		22 m

Height 		4000

Loading height 	5500

Width 		3845

Weight 		15000 kg

Central lubrication

HIGH TIP BUCKET

Capacity 		0.6 m3

Bucket depth 	670 mm

Tipping 		120°

Hydraulics		double-acting

Accessory		a sheet for fastening front loader’s quick connection parts

Working width 	2000 mm

Height 		680 mm

Weight 		325 kg

Usage applications

- Front loaders (addition to load height approximately 0.8 m)

- Fork-lifts (the possibility to use fork-lift as a bucket machine)

- Tractor’s lifter bucket

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

HIGH TIP BUCKET

Capacity 		1.5 m3

Bucket depth 	1000 mm

Tipping 		117°

Hydraulics		double-acting

Accessory		a sheet for fastening front loader’s quick connection parts

Working width 	2350 mm

Height 		830 mm

Weight 		550 kg

Usage applications

- Front loaders (addition to load height approximately 1 m)

- Fork-lifts (the possibility to use fork-lift as a bucket machine)

- Tractor’s lifter bucket

# Manufacturing and selling: 	RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

TANK TRAILER AND FIRE-FIGHTING EQUIPMENT FOR PEAT BOGS, FOREST FIRES, AND LAND FIRES

# RAISELIFT OY

Raivalantie 524

39920 SUOMIJÄRVI

FINLAND

tel. +358 2 544 4141, +358 400 126 332

fax +358 2 544 4241

seppo.lamminmaki@raiselift.inet.fi

www.raiselift.fi

Business ID: 1945243-7

TANK TRAILER AND FIRE-FIGHTING EQUIPMENT

- 3000-litre tank trailer with lockable cases in the back and on each sides, four tires 14.9 – 24 with tractor pattern, Raju rims, possibility of removing the outermost wheels and increasing the trailer’s width to 2.3 meters.

- Jurop pump on the drawbar which is rotated with tractor’s PTO. The pump endures silt and rough impurities of the size of 2 cm3 and does not need feeding water. The pump can be used for taking water either from the tank trailer or fire basin by changing hoses from quick couplings. At the same the pump can be used to fill up the tank. The trailer can be used for watering strip also during the drive by means of the quick fastened double mist nozzle.

- Tank trailer has been sand blasted, primed, and painted.

- Delivery includes also a cardan shaft for the pump.

- Fire-fighting equipment, which is placed as a whole in the tank trailer, is in accordance with peat site class III and includes:

      - fire hose 76 mm	300 m

      - fire hose 39 mm	400 m

      - fog jet pipe	3 pcs

      - splitter		1 pc

      - transition coupler	2 pcs

      - softener		60 l

      - shovel		4 pcs

      - bucket		6 pcs

      - combustion engine-powered pump Honda W 20 X

      - suction hoses and strainers

      - double fog nozzle	1 pcs

TANK TRAILER

- Bottom axis is the place for the cardan shaft.

- The pump is rotated at a 540 r/min PTO.

- The pump does not need feeding water.

- The pump has oil on the cog gearing’s side. Make sure that the cog gearing has oil.

- There are faucets in the suction tube for taking water either from the tank or from behind the tank with a suction tube. If water is taken from the tank, back suction tube’s faucet has to be closed and tank’s faucet open. If water is taken from the back with a suction tube, tank’s faucet has to be closed and back suction tube’s faucet open. Always make sure that either one of the faucets is open.

- The tank can be filled up by attaching a hose mounted in the tank to the pump’s pressure coupling and using the suction tube in the back.

- Empty water from the tank and pump bottom plug in the fall, lubricate the pump with a water and antifreeze mixture, dry the faucets and pipes with compressed air, leave the faucets open, also remember to empty combustion engine pump.

- Make sure that suction pipe seals are intact and safe.

- Tank trailer includes:

  - combustion engine hose

  - fire hose 76 mm	300 m

  - fire hose 39 mm	400 m

  - fog jet pipe	3 pcs

  - splitter		1 pc

  - transition coupler	2 pcs

  - softener		60 l

  - metal bucket	6 pcs

  - shovel		4 pcs

  - field watering nozzle

  - suction hoses

# Text boxes

BROACHING (12

DEEP 15 (1 PCS)

(FROM THE BACK)

PEAT PARTICLE